## Slide 1: Erebus Labs STEM Sensor
Scott Lawson – CpE
Chris Clary – EE
Max Cope – EE
Bryan Button – EE

## Slide 2
Introduction
Objective
Hardware
Software
Lessons Learned
Thoughts for Rev. 2
Q&A

## Slide 3
Introduction
Objective
Create an Environmental Sensor System
  Hardware/Software
  Documentation
Keep it Simple
Keep it Open
Keep it Cheap
Get Kids Interested in STEM!
Notes: Talking points:
%16 of American high school seniors are proficient in mathematics and interested in a STEM career

## Slide 4: Hardware

## Slide 5
Hardware
Hardware Overview

## Slide 6
Hardware
Main Board (Base Station)
Switching Power Supply
Sensor Port
PSoC 3 Microcontroller
USB Interface
Notes: Chris starts
Discuss GPs
Note power and interface and discuss in detail when they come up

## Slide 7
Hardware
Power Supply
Linear Power Supply
  Less Noise
  Lower Battery Life
Switching Power Supply
  Noise Not An Issue
  Better Battery Life
  One Part for 3V and 5V
  More Complex
Notes: Tradeoffs (LDO vs Swiching)
Switching regulators didn’t work on breadboard

## Slide 8
Hardware
Interfaces
Ethernet for Sensor Port
  Cheap Cables
  Easy to Work With
  Many Lengths Available
USB
  Standard for Most Computer Interface Applications
  Micro USB = Small Footprint
Notes: Ethernet:
Cheap cables are important for keeping costs low.
Easy to work with in consideration of use by children (not to hard to make your own cable).
Length kept in mind for future applications (e.g. sensor in a well)
More sensors could be put onto a single module
USB:

## Slide 9
Hardware
Low-Oxygen Sensor
Figaro TGS 2600
Technically “Air Contaminant Sensor”
Resemblance to VOC Sensor
Easy to Find Applications or Experiments
Notes: Labeled as an air contaminant sensor, the device senses contaminants due to the displacement of oxygen (or just normal breathing air) causing a change in the flow of electrons. Different sensitivity characteristics for different gasses.
Wanted to do a sensor that detected the quality of a substance similar to the original request for a VOC sensor for wells.
Experiments include things such as detecting change in air quality in high traffic areas over certain times or seeing how rapidly the quality of air changes when enclosed with a burning candle (and how long it takes for air to return to normal).

## Slide 10
Hardware
Light Sensor
Easy to Implement
Simple to Understand
Many Use Cases
Proof of Concept Sensor

## Slide 11
Hardware
Other
Two Buttons (Start & Stop)
LED System Indicator
  Start Sampling
  Stop Sampling
Powered with 4x AA Batteries

## Slide 12
Hardware
Cypress PSoC 3
Development Kit – Rapid Prototyping
Flexible Architecture
  Universal Digital Blocks
  Programmable Interconnects
One Chip Solution
  Real Time Clock
  USB Controller
  Hardware Emulation
Notes: Max starts

## Slide 13
Hardware
PSoC Architecture

## Slide 14: Software

## Slide 15
Software
PSoC Creator
Free Development Environment
Drag-and-Drop Programming
Extensive APIs

## Slide 16
Software
Firmware

## Slide 17
Software
Firmware
Serial Over USB
LED System Indicator
  Sample
  Error
  USB Connected
Max Speed 1 Sample Per Second
Notes: Errors:
* Low Battery (blink yellow)
* Memory Full (red)

## Slide 18
Software
Firmware
Emulated EEPROM
  Emulated Inside Flash
  Wear Leveling
Power Management
  No Power Switch
  Minimal Current Use
Timestamps Using Real Time Clock
Notes: Scott starts

## Slide 19
Software
GUI
Simple & Minimalistic
Sample Settings
Reference and Documentation

## Slide 20
Software
Software/Hardware Interaction

## Slide 21: Documentation
Notes: Hand out documents
Stop example experiment and process data

## Slide 22
Documentation
User Documents
Technical Reference Manual
System Architecture
User Manual
Fundamentals of Electronics
Notes: Start handing out documentation

## Slide 23
Documentation
Project Documents
Design Specification
Budget
Timeline
Requirements
Test Plan

## Slide 24: Lessons Learned (Thoughts for Rev. 2)
Notes: Bryan starts

## Slide 25
Thoughts
Lessons Learned
Don’t Focus on Single-Chip Solution
  Distribution = Power Savings
Use Separate EEPROM
  Storage not Lost Due to Firmware Size
  Wear Leveling
Use Off-Chip RTC
  Button-Cell Battery Backup
Notes: Current RTC loses time when power is lost

## Slide 26
Thoughts
Revision 2
Critical Battery Shutdown
Enclosure Mounted Buttons
Power-Wire Strain Relief
Weather Proof Box
VOC Sensor
Multiple Sensor Ports
Jumper for Power

## Slide 27: Q&A
Notes: Answer questions