## Slide 1: Erebus Labs STEM Sensor
Scott Lawson – CpE
Chris Clary – EE
Max Cope – EE
Bryan Button – EE

## Slide 2: Hardware

## Slide 3
Hardware
Main Board (Base Station)
Switching Power Supply
Sensor Port
PSoC 3 Microcontroller
USB Interface

## Slide 4
Hardware
Cypress PSoC 3
Development Kit – Rapid Prototyping
Flexible Architecture
  Universal Digital Blocks
  Programmable Interconnects
One Chip Solution
  Real Time Clock
  USB Controller
  Hardware Emulation

## Slide 5
Hardware
PSoC Architecture

## Slide 6
Hardware
Power Supply
Linear Power Supply (First Choice)
  Less Noise
  Lower Battery Life
Switching Power Supply
  Noise not an issue
  Battery life more important
  Smaller Footprint
  One Part for 3V and 5V

## Slide 7
Hardware
Interfaces
Ethernet for Sensor Port
  Cheap Cables
  Easy to Work With
  Many Lengths Available
USB
  Standard for Most Computer Interface Applications
  Micro USB = Small Footprint
Notes: Ethernet:
Cheap cables are important for keeping costs low.
Easy to work with in consideration of use by children (not to hard to make your own cable).
Length kept in mind for future applications (e.g. sensor in a well)
USB:

## Slide 8
Hardware
Sensor Modules
Low-Oxygen Sensor
Light Sensor

## Slide 9
Hardware
Low-Oxygen Sensor
Figaro TGS 2600
Technically “Air Contaminant Sensor”
Resemblance to VOC Sensor
Easy to Find Applications or Experiments
Picture of Sensor Module
Notes: Labeled as an air contaminant sensor, the device senses contaminants due to the displacement of oxygen (or just normal breathing air) causing a change in the flow of electrons. Different sensitivity characteristics for different gasses.
Wanted to do a sensor that detected the quality of a substance similar to the original request for a VOC sensor for wells.
Experiments include things such as detecting change in air quality in high traffic areas over certain times or seeing how rapidly the quality of air changes when enclosed with a burning candle (and how long it takes for air to return to normal).

## Slide 10
Hardware
Light Sensor
Easy to Implement
Simple to Understand
Many Use Cases
Proof of Concept Sensor
Picture of Sensor Module

## Slide 11
Hardware
Other
Two Buttons (Start & Stop)
LED System Indicator
  Start Sampling
  Stop Sampling
Powered with 4x AA Batteries
Mixed Ground Planes (Analog/Digital)

## Slide 12: Software

## Slide 13
Software
PSoC Creator
Free Development Environment
Drag-and-Drop Programming
Extensive APIs

## Slide 14
Software
Firmware
Serial Over USB
Max Speed 1 Sample Per Second
LED System Indicator
  Sample Get
  Errors
  USB Connected
  Low Battery

## Slide 15
Software
Firmware
Emulated EEPROM
  Emulated Inside Flash
  Wear Leveling
Power Management
  No Power Switch
  Minimal Current Use
Timestamps Using Real Time Clock

## Slide 16
Software
GUI

## Slide 17
Software
GUI
Simple & Minimalistic
Sensor Selection
Sample Rate
Reference and Documentation
Auto-Clear Data on Successful Dump
Written in Python

## Slide 18: Lessons Learned (Thoughts for Rev. 2)

## Slide 19
Thoughts
Components
Use Separate EEPROM
  Storage not Lost Due to Firmware Size
Use Off-Chip RTC
  Button-Cell Battery Backup

## Slide 20
Thoughts
Revision 2
Critical Battery Shutdown
  Predictable Low-Power Operation
Power-Wire Strain Relief
Weather Proof Box
VOC Sensor
Multiple Sensor Ports
Jumper for Power

## Slide 21: Q&A